CALIFORNIA ENVIRONMENTAL QUALITY ACT

STATEMENT OF SUPPORT

CLASS 32 (INFILL DEVELOPMENT) EXEMPTION DETERMINATION

6141-6191 Atlantic Avenue

Application No. 1706-11

October 4, 2018

Section 15300 through 15333 of the California Environmental Quality Act (CEQA) establishes certain classes of projects as categorically exempt from the provisions of CEQA because they do not ordinarily result in a significant effect on the environment.  The Project proposes to remodel and expand by 16,352 square-feet an existing commercial shopping center with two restaurants with drive-through lanes supported by 134 parking stalls on a 112,406 square-foot site located at 6141-6191 Atlantic Avenue in the Commercial Neighborhood Automobile-Oriented District (CNA).

CEQA Section 15300.2 provides specific instance where exceptions to the established Classes of Exemptions included Class 32 -Infill Exemption are superseded; none of those conditions were found to apply to this project. The following analysis provides substantial evidence to support a conclusion that the proposed project qualifies for an exemption under CEQA Guidelines Section 15332 as a Class 32 urban infill development, and would not have a significant effect on the environment.

- THE PROJECT IS CONSISTENT WITH THE APPLICABLE GENERAL PLAN DESIGNATION AND ALL APPLICABLE GENERAL PLAN POLICIES AS WELL AS WITH APPLICABLE ZONING DESIGNATION AND REGULATIONS.

The project site is zoned Commercial Neighborhood Automobile Oriented (CNA) District; a designation that permits retail and service uses.  This Zoning designation is consistent with the General Plan Land Use Designation (LUD) of LUD #8A Traditional Retail Strip Commercial.  The project is designed to comply with all development standards and implements the General Plan objectives to provide adequate off-site parking, minimize the number of curb cuts, and designs commercial structures that are sensitive to nearby residential uses through its site configuration.

- THE PROPOSED DEVELOPMENT OCCURS WITHIN CITY LIMITS ON A PROJECT SITE OF NO MORE THAN FIVE ACRES SUBSTANTIALLY SURROUNDED BY URBAN USES.

The project site is entirely within the city limits of Long beach, on a site that is 2.58 acres in size which is less than maximum five acres specified.  The project site is  bounded by Atlantic Avenue to the east, Linden Avenue to the west, 61st Street to the south, and Harding Street to the north.  The project site is an existing shopping center and adjacent vacant parcel. The surrounding streets separate the project site form a range of urban uses including both commercial and residential land uses.

- THE PROJECT SITE HAS NO VALUE AS HABITAT FOR ENDANGERED, RARE OR THREATENED SPECIES

The project site is a formerly developed site that that has not value as, a habitat for endangered rare or threatened species.

- APPROVAL OF THE PROJECT WOULD NOT RESULT IN ANY SIGNIFICANT EFFECTS RELATING TO TRAFFIC, NOISE, AIR QUALITY, OR WATER QUALITY.

The project will not result in any significant effects relating to traffic within the area or on the local streets as detailed in the Traffic Impact Analysis prepared by Linscott Law & Greenspan and is incorporated by reference here.

The Project’s emissions were calculated using CalEEmod V.2061.3.2 and is incorporated by reference here.  Both emissions for construction and operation were found to be below the thresholds of significance for the six criteria pollutants established by the South Coast Air Quality Management District. Therefore, there are not significant effects relating to traffic are anticipated.

The ambient noise environment of the Project site consists primarily of traffic noise from the adjacent streets and the 91 Freeway located north of the project site.  Short term noise levels associated with construction will comply with the City’s Noise ordinance.  Operational noise associated with the shopping center would be generated by vehicles, doors, car alarms, and peoples talking as is typical of commercial shopping centers.  At the time of operation, the shopping center will not introduce a substantial new noise source relative to existing conditions and the project will operate within the standards of the adopted Noise Ordinance. Furthermore, the project has been condition to prohibit noise levels from the project to exceed the noise standards specified in the Long Beach Municipal Code.

Furthermore, the proposed project will comply with all requirement of the Long Beach Municipal Code Chapter 18.74 pertaining to low impact development standards and practices for stormwater pollution mitigation.

- THE SITE CAN BE ADEQUATELY SERVED BY ALL REQUIRED UTILITIES AND PUBLIC SERVICES.

The project was previously developed and served by utilities and public services.  The Project can adequately be served by utilities and public by reestablishing connections for water, sewer, electrically and natural gas, which would be undertaken as part of the building permitting process.