Residential Unit Violations

- Are smoke alarms installed and maintained in all bedrooms and hallways leading to bedrooms? Have batteries been replaced?

- Is there a minimum of one residential type ABC fire extinguisher provided within the residence, at an accessible location?

- Are dryer vent exhaust duct attached and in good condition?

- Has lint and debris been removed from behind dryers and dryer screens?

- Has excess combustible materials and flammable liquids, for maintenance (over 5 gallons) been removed from residence and garage?

- Are extension cords used for permanent wiring, if so remove? A single power strip is acceptable.

- Is power strip in good working condition with no visible signs of damage?

- Entry doors are not provided with double-keyed dead bolts?

Common Area Violations

- Are fire apparatus access roads unobstructed?

- Are fire lanes identified with signs or red painted curbs?

- Are building address numbers legible and visible from the street?

- Is a Knox box provided, and all included keys current?

- Have obstructions been removed from exit paths?

- Are exit doors operable from the inside without a key or special knowledge or effort?

- Are exit doors in operational condition?

- Are there locking devices of any kind installed on exit doors, other than locks integrated with panic hardware?

- Has storage been removed from under unsprinklered stairways?

- Are exit signs installed in rooms or areas, which require two or more exits, and at locations leading to a public way? Do all exit signs function?

- Are low level exit signs installed in interior rated corridors? Do all low level exit signs function?

- Has emergency lighting been installed in all common areas, including stairs? Does all emergency lighting function?

- Are fire extinguishers located in accessible locations and identified?

- Is there a minimum of one 2A-10BC fire extinguisher located within a 75ft travel distance?

- Is the fire alarm system in an operable condition?

- Are fire departments connections, standpipes, and fire hydrants unobstructed?

- Do the fire alarm, fire hydrants and standpipe systems have current certifications?

- Are electrical and gas meters labeled?

- Is there a clear space in front of electrical panels of 30in wide, by 36in deep and 76in in height?

- Is electrical wiring maintained in good condition?

- Are extension cords used for permanent wiring, if so remove?

- Are there open junction boxes or wiring, if so repair?

- Are all switches, outlet boxes and electrical panel breakers, provided with approved covers?

- Are fire doors unobstructed and close from the full open position and latch automatically?

- Have all holes in fire rated construction been repaired?

- Are flammable and combustible liquids exceeding 10 gallons stored in liquid storage cabinets?

- Has combustible storage been removed from and around exit paths?

- Has all combustible material and flammable liquids been removed from boiler, mechanical and electrical rooms and garages, and common areas?

- Are dryer vent exhaust duct attached and in good condition?

- Has lint and debris been removed from behind dryers and dryer screens?

- Has all waste and rubbish materials been removed from the premises?

- Dumpsters and containers shall not be stored in buildings or placed within 5ft of combustible walls, openings, or under roof eave lines, unless provided with automatic sprinklers.

- Is there 30 feet of clearance of all flammable vegetation or other combustible growth around and adjacent to the occupied dwelling or occupied structure?

- Has the fire safety and evacuation plan been updated and approved by the fire department?

- Has the annual fire evacuation drill been completed?

- Has the bi-annual fire extinguisher training been completed?

- Are automatic external defibrillators (AED) provided on each floor? Has training been provided to responsible parties?

- Has fire department approved evacuation signage been mounted at all stairways, elevators and within the main entrance?

- Is life saving rescue equipment provided on floors as approved by the fire department

- Has the building owner, homeowners association or the property management company sent the ‘Self Certification” letter to the fire department annually?

# Text boxes

### This brochure is being provided to assist property owners in performing a fire and life safety “self inspection”, prior to the annual inspection conducted by the fire department. The items listed within this brochure represent common Fire Code violations found during Residential Occupancy Inspections. The brochure has been separated in two parts, one for the interior residential units and one for the remainder of the buildings common areas. All items listed may not apply to every occupancy; therefore utilize their intent towards fire and life safety at your location.

. . . more than fighting fires

Since 1897